## Slide 1
SMART HOME SECURITY SYSTEM
Design and Simulation
of a Smart Home Security System
Presented by group -11
Project in One Sentence
A circuit that checks door, window, and motion sensors, counts active sensors, selects a security rule, and turns on an alarm only when armed.
Final 1-bit output: 1 = alarm ON, 0 = alarm OFF
Jasmitha - 2620040033 Harshini - 2620040066 Harshith – 262004011
Lohith - 2620040023

## Slide 2
FOUNDATION
Introduction and Objective
What problem are we modelling, and what should the circuit do?
Introduction
A home can have several possible entry points. Door, window, and motion sensors provide simple ON/OFF signals. Digital logic combines these signals to decide whether a possible intrusion should trigger an alarm.
Project Objective
Build a digital circuit that counts active sensors, applies one of two security rules, and blocks the alarm whenever the system is disarmed.
Output and Rule
Alarm output: 1 = alarm ON; 0 = alarm OFF. The alarm sounds only when the system is armed and the selected security condition is satisfied.
Logic convention: A logic value of 1 means ON/active and a logic value of 0 means OFF/inactive throughout this project.
Sensor Inputs
Door (D)
1 = open; 0 = closed
Window (W)
1 = open; 0 = closed
Motion (M)
1 = movement detected; 0 = no movement
Control Inputs
Arming Switch
1 = security ON; 0 = OFF
Mode Selector
0 = normal mode; 1 = strict mode

## Slide 3
LOGIC MODEL
Theory and Logic Circuit
How the sensor counter and security decision work
1. Half-Adder 1 — Inputs: Door (D) and Window (W)
Output | Expression | Meaning
Sum₁ | D XOR W | 1 when inputs differ
Carry₁ | D AND W | 1 when both are 1
2. Half-Adder 2 — Inputs: Sum₁ and Motion (M)
Output | Expression | Meaning
CountLow | Sum₁ XOR M | Low bit of sensor count
Carry₂ | Sum₁ AND M | Second carry signal
3. OR Gate — Count High Bit
CountHigh = Carry₁ OR Carry₂
The two bits together count active sensors from 0 to 3:
Circuit Diagram Placeholder
Half-Adder 1 Half-Adder 2 OR Gate AND Gate

## Slide 4
IMPLEMENTATION
Circuit Design in Logisim
Implementation, signal path, and Boolean expression
Signal Path
01
Sensor Inputs
Door, window, and motion inputs enter the circuit
02
Half-Adder 1
D + W → produces Sum₁ and Carry₁
03
Half-Adder 2
Sum₁ + M → produces CountLow and Carry₂
04
OR Gate
Combines Carry₁ and Carry₂ to form CountHigh
05
Multiplexer
Selects normal or strict rule based on Mode selector
06
AND Gate
Combines selected signal with Armed switch
07
Alarm Output
Final 1-bit alarm result
Boolean Expressions
Signal | Expression
CountLow | (D XOR W) XOR M
CountHigh | (D AND W) OR ((D XOR W) AND M)
Normal condition | CountHigh OR CountLow
Strict condition | CountHigh
Selected alarm | MUX(Normal, Strict, Mode)
Alarm | Armed AND Selected alarm
Select = 0 chooses normal mode; Select = 1 chooses strict mode. The selector does not arm the system.

## Slide 7
VERIFICATION
Simulation Results
Truth Table — Sensor Count vs. Mode
Active Sensors | Count (High, Low) | Normal Mode | Strict Mode
None | 0 0 | OFF | OFF
One sensor | 0 1 | ON | OFF
Two sensors | 1 0 | ON | ON
Three sensors | 1 1 | ON | ON
Strict modetriggers for 1, 2, or 3 active sensors. Normal mode
triggers only for 2 or 3 active sensors.
How to Test
Arm the System
Set Armed = 1 to test alarm responses
Change Mode
Mode = 0 for normal; Mode = 1 for strict
Disarm Test
With Armed = 0, alarm is OFF for every sensor combination
Troubleshoot
If output differs, check the MUX select pin, sensor inputs, and arming switch
Truth Table / Extra Test Evidence Placeholder
Insert your full truth table or additional Logisim screenshots here. Include the three sensor inputs, mode selection, arming switch, and expected alarm output.

## Slide 8
CLOSE
Conclusion and Applications
Conclusion
Sensors represent doors, windows, and movement in a protected area.
Half-adders count the active sensors; the OR gate combines carry signals.
The multiplexer selects normal or strict mode.
The final AND gate ensures the alarm only works when armed.
The project demonstrates half-adders, XOR, OR, AND, and multiplexer logic in one design.
Applications
Homes & Apartments
Laboratories & Offices
Small Storage Rooms
The same logic concept can be adapted to other protected areas.
Possible Improvements
Siren / Notification Output
Add a real siren or notification output for physical alerting
More Sensors
Include additional sensor inputs to cover more entry points
Delay or Entry Code
Add a delay timer or PIN-based entry code for usability
Real Hardware
Test the circuit with real hardware after safe design review
Limitation
This is a digital logic simulation, not a complete real alarm. A real installation also needs physical sensors, power, a siren driver, and safe installation.